## Slide 1: CS450 Tutorial Session 1
Android and IOIO Board

## Slide 2: An Overview of Tricorder
Android Phone
IOIO Board
Tmote(Bridge)
Tmote(Probe)
Sensors
*Tmote=telosb
*Android Phone=Droid

## Slide 3: Why we need IOIO Board?
A pervasive device: Android Phone
Need a low power radio to control and communicate with a Tmote
How? The answer is IOIO Board.

## Slide 4: What is an IOIO Board
The IOIO (pronounced "yo-yo") is a board specially designed to work with an Android device to provide extensive and robust connectivity to an Android device via a USB connection.
In this semester we’ll use IOIO Board to connect an Android phone and a Tmote through serial connections. (Android to IOIO Board through Android Debug Bridge(ADB) and IOIO Board to Tmote through Uart)
*IOIO Board need a 5-15V 1A power supply. In this project we use both Droid and Tmote(bridge) to supply the power for IOIO Board. Since Tmote(bridge) only provide 500mA of maximum output current, you need to make sure your Droid is fully charged.

## Slide 5: Create an Android Project
While Learning to set up Eclipse-ADK and TinyOS Dev-Env is highly recommended, we provide a Ready-To-Use Vmware Image with which you can load onto your vmware player andAll those environment things are setup for you with one-click and tutorials already loaded into the Eclipse.

## Slide 6: Start Eclipse on the desktop

## Slide 7: Create an Android Project
  Menu: File->New->Project
  From "Android" Select Android Project (Fig 1)

## Slide 8: Create an Android Project
  Type in the "Project Name" with HelloMyCS450
  In "Build Target" Select "Android 2.2"
  Scroll Down the Window
  In "Properties" fill in "Package name" with "com.example"
  Click on "Finish"

## Slide 9: Run an Android Project

## Slide 10: A glance at a Hello World

## Slide 11: Import an Android Project
In Java Perspective, Menu: File->Import
In Window titled "Select" select "General->Existing Project into Workspace", Click on "Next"
In "Select Root root directory" click on Browse and select the project your want to import. Click on "Finish"

## Slide 12: Import an Android Project
Browse into the directory of an Android Project and Click on “OK”

## Slide 13: Basic UI components
TextView
Button and EditText
Layouts

## Slide 14: Android “Activity”
What is an Activity
Activity is the base class of a fundamental page in an Android application
Runs like a thread, but...

## Slide 15: Android “Message”
How does an Activity talk to anther one?
  Operating System maintain a Message Queue
  Upon arrival of each message, do a “switch case”
  In Activity A:
  declare “Handler mHandler =new Handler(){
  public void handleMessage(Message msg){
      switch (Message msg.what)”
      {
      case I_AM_HUNGRY:
        Make_some_food();
        break;
      case I_AM_THIRSTY:
        Get_some_drinks();
        break;
      default:
        do_nothing();
  } } }
  In Activity B:
  ...
  Message msg=new Message();
  msg.what=I_AM_HUNGRY;
  msg.obj=new String(“What I want”);
  A.mHandler.sendMessage(msg);

## Slide 16: Launch HelloIOIO and HelloIOIOUart
Classroom Demo
Video Demo on Youtube
  http://www.youtube.com/watch?v=PLlAtjLKtrQ
1. Connect a tmote to a USB port which is used as an external power supply for IOIO Board
2. Connect droid to the PC, click on the “run” icon
3. When the application is running on a droid, disconnect the PC and connect to the IOIO Board
4. You should be able to see LED on IOIO Board blinking and the command line on Droid is printing data.

## Slide 17: Warming up exercise
Implement an EditText with an “Enter” Button that user can type in and print it to a TextView like a command line

## Slide 18: Quetions?
or mailto: zzn@jhu.edu
Zainan Victor Zhou